## Slide 1: Forecasting algal blooms in Falling Creek Reservoir

## Slide 2
Adaptation: R. Quinn Thomas et al.
Real-time sensor
Input data
Model output: 1- and 2-week forecasts of chlorophyll-a
Chl-a Model
25%
75%
95%
Mon
Tues
Weds
Thurs
0%
16-day weather forecast
Forecast for managers & decision support tools
Historical observational data
FLARE (Forecasting Lake And Reservoir Ecosystems)
Data assimilation and Forecasting Workflow
Notes: To summarize the workflow of one day of our forecasting system, which is called FLARE (Forecasting Lake and Reservoir Ecosystems), meteorological sensor data being recorded every minute stream to a server that make the data available on github, a data storage website. These data are used to run a lake model for one day, which generates model output that are compared with observational data and used to update the model. The updated model serves as the initial conditions for the next day’s simulation, which are fed by NOAA’s 16-day GEFS meteorological forecast, which is used as driver data to generate a water quality forecast for the next 16-days.

## Slide 3
Q1: How well can we forecast near-term algal biomass (chlorophyll-a) using an empirical model approach?
Observed
Forecast mean
95% Confidence Interval
Total R2 = 0.38
Total RMSE = 6.5 μg/L
Non-bloom* R2 = 0.44
Non-bloom* RMSE = 1.9 μg/L
*outside dotted lines

## Slide 4
Chl-at = β1 + β2Chl-at-1 – β3Discharget – β4Shortwavet + Ɛ
Process uncertainty
Meteorological driver uncertainty
21 NOAA forecast ensembles
Discharge driver uncertainty
Parameter uncertainty
Initial condition uncertainty
What are the dominant drivers of uncertainty in our forecasts?
βx

## Slide 5
Relative proportion of uncertainty changes throughout the time series
Notes: Add legend

## Slide 6: Effectively Visualizing Forecast Output
a) All ensembles shown + forecast mean
b) Mean + CI (extrinsic)
c) Polygon of entire CI (intrinsic)
d) Animation of forecast mean + CI through time up to present
e) Interactive app that allows user to visualize in multiple ways
Time into future
Chl-a (ug/L)
Time into future
Chl-a (ug/L)

## Slide 7
Heterogeneity among reservoir continua
2 reservoirs
5 streams
17 sites total
6 sampling days
Q1: What is the longitudinal heterogeneity of nitrogen, phosphorus, and chlorophyll-a along a double reservoir continuum?
Q2: What are the drivers of heterogeneity among reservoir continua (i.e., residence time, internal loading)?

## Slide 8: Looooots of field sampling and teamwork!

## Slide 9
FCR and BVR exhibit seasonal trends and heterogeneity between reservoirs

## Slide 10: FCR and BVR exhibit similar increasing trend over time but different magnitude in amount of increase
Why?
  Weather is consistent btw them
  Residence time?
    Working on rough water budgets
  Nutrients from inflows forthcoming
    FCR receiving nutrients from BVR?
    Internal loading?